## Slide 1: Applications/Example

## Slide 2
Overview
Memory Hierarchy
Main Memory
Auxiliary Memory
Associative Memory
Cache Memory
Virtual Memory
Parallel Computing
Pipelining
Multiprocessors
Interconnection Structures

## Slide 3
Memory Hierarchy
Magnetic
tapes
Magnetic
disks
I/O
processor
CPU
Main
memory
Cache
memory
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape
Memory Hierarchy is to obtain the highest possible access speed.
While minimizing the total cost of the memory system.

## Slide 4
Main Memory
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus

## Slide 5
Memory Address Map
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
RAM 1
RAM 2
RAM 3
RAM 4
ROM
0000 - 007F
0080 - 00FF
0100 - 017F
0180 - 01FF
0200 - 03FF
Component
Hexa
address
0 0 0 x x x x x x x
0 0 1 x x x x x x x
0 1 0 x x x x x x x
0 1 1 x x x x x x x
1 x x x x x x x x x
10 9 8 7 6 5 4 3 2 1
Address bus
Memory Connection to CPU
RAM and ROM chips are connected to a CPU through the data and address buses
The low-order lines in the address bus select the byte within the chips
And other lines in the address bus select a particular chip through its chip select inputs

## Slide 6
Connection of Memory to CPU
CS1
CS2
RD
WR
AD7
128 x 8
RAM 1
CS1
CS2
RD
WR
AD7
128 x 8
RAM 2
CS1
CS2
RD
WR
AD7
128 x 8
RAM 3
CS1
CS2
RD
WR
AD7
128 x 8
RAM 4
Decoder
3
2
1
0
WR
RD
9
8
7-1
10
16-11
Address bus
Data bus
CPU
CS1
CS2
512 x 8
ROM
AD9
1- 7
9
8
Data
Data
Data
Data
Data

## Slide 7
Auxiliary Memory
Information Organization on Magnetic Tapes
EOF
IRG
block 1 block 2
block 3
block 1
block 2
block 3
R1
R2 R3 R4
R5
R6
R1
R3 R2
R5 R4
file i
EOF
Organization of Disk Hardware
Track
Moving Head Disk Fixed Head Disk

## Slide 8
Associative Memory
Argument register(A)
Key register (K)
Associative memory
array and logic
m words
n bits per word
Match
register
Input
Read
Write
M
- Accessed by the content of the data rather than by an address
- Also called Content Addressable Memory (CAM)
Hardware Organization

## Slide 9
Organization of CAM
Internal organization of a typical cell Cij
C11
Word 1
Word i
Word m
Bit 1
Bit j
Bit n
M1
Mi
Mm
Aj
R
S
Output
Match
logic
Input
Write
Read
Kj
M
i
To
F
ij
K1
Kj
Kn
C1j
C1n
Ci1
Cij
Cin
Cm1
Cmj
Cmn
A1
Aj
An
i= word
j-= bit in word

## Slide 11
Cache Memory
Locality of Reference
- The references to memory at any given time interval tend to be confined within a localized areas.
- This area contains a set of information and the membership changes gradually as time goes by.
- Temporal Locality
The information which will be used in near future is likely to be in use already
( e.g. Reuse of same address or information in loops)
- Spatial Locality
If a word is accessed, adjacent(near) words are likely accessed soon
(e.g. Related or nearby data items (arrays) are usually stored together; instructions are executed sequentially)

## Slide 12
Cache Memory
Cache
- The property of Locality of Reference makes the cache memory systems work
- Cache is a fast small capacity memory that should hold those information
which are most likely to be accessed
Main memory
Cache memory
CPU

## Slide 13
Performance of Cache
All the memory accesses are directed first to Cache
If the word is in Cache; Access cache to provide it to CPU
If the word is not in Cache; Bring a block (or a line) including that word to replace a block now in Cache
- How can we know if the word that is required is there ?
- If a new block is to replace one of the old blocks, which one should we choose ?
Memory Access

## Slide 14
Performance of Cache
Performance of Cache Memory System
Hit Ratio - % of memory accesses satisfied by Cache memory system
Te: Effective memory access time in Cache memory system
Tc: Cache access time
Tm: Main memory access time
Te = Tc + (1 - h) Tm
Example: Tc = 0.4 s, Tm = 1.2s, h = 0.85%
Te = 0.4 + (1 - 0.85) * 1.2 = 0.58s

## Slide 15
Memory and Cache Mapping –
(Associative Mapping)
Associative mapping
Direct mapping
Set-associative mapping
Mapping Function
Specification of correspondence between main memory blocks and cache blocks
They are of three types:

## Slide 16
Memory and Cache Mapping –
(Associative Mapping)
Associative Mapping
- Any block location in Cache can store any block in memory
-> Most flexible
- Mapping Table is implemented in an associative memory
-> Fast, very Expensive
- Mapping Table
Stores both address and the content of the memory word
address (15 bits)
Argument register
Address
Data
0 1 0 0 0
0 2 7 7 7
2 2 2 3 5
3 4 5 0
6 7 1 0
1 2 3 4
CAM

## Slide 17
Cache Mapping – Direct mapping
- Each memory block has only one place to load in Cache
- Mapping Table is made of RAM instead of CAM
- n-bit memory address consists of 2 parts; k bits of Index field and n-k bits of Tag field
- n-bit addresses are used to access main memory and k-bit Index is used to access the Cache
Addressing Relationships
Direct Mapping Cache Organization
Memory
address
Memory data
00000
1 2 2 0
00777
01000
01777
02000
02777
2 3 4 0
3 4 5 0
4 5 6 0
5 6 7 0
6 7 1 0
Index
address
Tag
Data
000
0 0
1 2 2 0
0 2
6 7 1 0
777
Cache memory
Tag(6) Index(9)
32K x 12
Main memory
Address = 15 bits
Data = 12 bits
512 x 12
Cache memory
Address = 9 bits
Data = 12 bits
00 000
77 777
000
777
n -k
k

## Slide 18
Addressing Relationships
Direct Mapping Cache Organization
Memory
address
Memory data
00000
1 2 2 0
00777
01000
01777
02000
02777
2 3 4 0
3 4 5 0
4 5 6 0
5 6 7 0
6 7 1 0
Index
address
Tag
Data
000
0 0
1 2 2 0
0 2
6 7 1 0
777
Cache memory
Tag(6) Index(9)
32K x 12
Main memory
Address = 15 bits
Data = 12 bits
512 x 12
Cache memory
Address = 9 bits
Data = 12 bits
00 000
77 777
000
777
n -k
k

## Slide 19
Cache Mapping – Direct mapping
Operation
- CPU generates a memory request with (TAG;INDEX)
- Access Cache using INDEX ; (tag; data)
Compare TAG and tag
- If matches -> Hit
Provide Cache(data) to CPU
- If not match -> Miss
Search main memory and replace the block from cache memory
Direct Mapping with block size of 8 words
000
0 1
3 4 5 0
007
0 1
6 5 7 8
010
017
770
0 2
777
0 2
6 7 1 0
Block 0
Block 1
Block 63
Tag Block Word
INDEX

## Slide 20
Cache Mapping –
Set Associative Mapping
Set Associative Mapping Cache with set size of two
- Each memory block has a set of locations in the Cache to load
Index
Tag
Data
000
0 1
3 4 5 0
0 2
5 6 7 0
Tag
Data
777
0 2
6 7 1 0
0 0
2 3 4 0

## Slide 21
Writing into Cache Concepts
Cache Write : Write Through and write Back
Write Through
  When writing into memory
If Hit, both Cache and memory is written in parallel
If Miss, Memory is written
  For a read miss, missing block may be overloaded onto a cache block
Memory is always updated
-> Important when CPU and DMA I/O are both executing
Slow, due to the memory access time

## Slide 22
Cache Write
Write-Back (Copy-Back)
  When writing into memory
If Hit, only Cache is written
If Miss, missing block is brought to Cache and write into Cache
  For a read miss, candidate block must be written back to the memory
Memory is not up-to-date, i.e.,
The same item in Cache and memory may have different value

## Slide 23
VIRTUAL MEMORY

## Slide 24
Virtual Memory
Give the programmer the illusion that the system has a very large memory, even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual address
Virtual
address
register
Memory
mapping
table
Memory table
buffer register
Main memory
address
register
Main
memory
Main memory
buffer register
Physical
Address

## Slide 25
Address Mapping
Organization of memory Mapping Table in a paged system (Page and line no.)
Address Space and Memory Space are each divided into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 3
Block 2
Block 1
Block 0
Address space
N = 8K = 213
Memory space
M = 4K = 212
0
000
1
001
1
010
0
011
0
100
1
101
1
110
0
111
1
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table
address
Presence
bit
Page no.
Line number
Virtual address
Main memory
address register
Memory page table
Main memory
11
00
01
10
01

## Slide 26
Associative Memory Page Table
Assume that
Number of Blocks in memory = m
Number of Pages in Virtual Address Space = n
Page Table
- Straight forward design -> n entry table in memory Inefficient storage space utilization
<- n-m entries of the table is empty
- More efficient method is m-entry Page Table
Page Table made of an Associative Memory
m words; (Page Number: Block Number)
1 0 1
Line number
Page no.
Argument register
1 0 1 0 0
0 0 1 1 1
0 1 0 0 0
1 0 1 0 1
1 1 0 1 0
Key register
Associative memory
Page no.
Block no.
Virtual address
Page Fault
Page number cannot be found in the Page Table

## Slide 27
Page Replacement
Decision on which page to displace to make room for an incoming page when no free frame is available
2
f
0
v
i
f
v
frame
valid/
invalid bit
page table
change to
invalid
4
reset page
table for
new page
victim
1
swap
out
victim
page
3
swap
desired
page in
backing store
physical memory

## Slide 28
Page Replacement
Modified page fault service routine
  1. Find the location of the desired page on the backing store
  2. Find a free frame
  - If there is a free frame, use it
  - Otherwise, use a page-replacement algorithm to select a victim frame
  - Write the victim page to the backing store
  3. Read the desired page into the (newly) free frame
  4. Restart the user process
2
f
0
v
i
f
v
frame
valid/
invalid bit
page table
change to
invalid
4
reset page
table for
new page
victim
1
swap
out
victim
page
3
swap
desired
page in
backing store
physical memory

## Slide 29
Page Replacement Algorithms
FIFO
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
-
FIFO algorithm selects the page that has been in memory the longest time.
Using a queue - every time a page is loaded, its identification is inserted in
the queue.
Easy to implement.
May result in a frequent page fault.
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames

## Slide 30
Page Replacement Algorithms
- LRU uses the recent past as an approximation of near future.
Replace that page which has not been
used for the longest period of time
LRU
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
LRU may require substantial hardware assistance.
The problem is to determine an order for the frames defined by the time of last use.

## Slide 31
Parallel Computers
Architectural Classification
Flynn's classification
Based on the multiplicity of Instruction Streams and Data Streams
Instruction Stream
  Sequence of instructions read from memory
Data Stream
  Operations performed on the data in the processor
 |  | Number of Data Streams | 
 |  | Single | Multiple
Number of Instruction Streams | Single | SISD | SIMD
 | Multiple | MISD | MIMD

## Slide 32
SISD
Characteristics
Single computer containing a control unit, processor and memory unit
- Instructions and data are stored in memory and executed sequentially
may or may not have parallel processing
- parallel processing can be achieved by pipelining

## Slide 33
SIMD

## Slide 34
MISD

## Slide 35
MIMD

## Slide 36
Pipelining
A technique of decomposing a sequential process into sub operations, with each sub process being executed in a special dedicated segment that operates concurrently with all other segments.
It is the characteristic of pipelining that several computations can be in progress in distinct segments at the same time.
Each segment performs partial processing dictated by the way the task is dictated
The result obtained from computation is in each segment is transferred to next segment in the pipeline
The final result is obtained after data has been passed through all segment

## Slide 37
Pipelining

## Slide 38
Design of a basic pipeline
•In a pipelined processor, a pipeline has two ends, the input end
and the output end. Between these ends, there are multiple stages/segments such that output of one stage is connected to input of next stage and each stage performs a specific operation.
•Interface registers are used to hold the intermediate output between two stages. These interface registers are also called latch or buffer.
•AII the stages in the pipeline along with the interface registers are
controlled by a common clock.

## Slide 39
Pipeline Stages
RISC processor has 5 stage instruction pipeline to execute ali the instructions in the RISC instruction
set. Following are the 5 stages of RISC pipeline with their respective operations:
Stage 1 (Instruction Fetch)
In this stage the CPU reads instructions from the address in the memory whose value is present in the
program counter.
Stage 2 (Instruction Decode)
In this stage, instruction is decoded and the register file is accessed to get the values from the registers used in the instruction.

## Slide 40
Pipeline Stages
Stage 3 (Instruction Execute)
In this stage, ALU operations are performed.
Stage 4 (Memory Access)
In this stage, memory operands are read and written from/to the memory that is present in the
instruction.
Stage S (Write Back)
In this stage, computed/fetched value is written back to the register present in the instruction.

## Slide 41
Operations in each Pipeline Stage

## Slide 42
General Pipelining

## Slide 43
Pipelining speed up

## Slide 44
Pipelining speed up

## Slide 45
Pipeline Stages
An ISA describes the design of a Computer in terms of the basic operations it must support. The ISA is not concerned with the implementation specific details of a computer. It is only concerned with the set or collection of basic operations the computer must support.
For example the AMD Athlon and the Core 2 Duo processors have entirely different implementations but they support more or less the
same set of basic operations as defined in the x86 Instruction Set.
Micro architectural level lies just below the ISA level and hence is concerned with the implementation of the basic operations to be supported by the Computer as defined by the ISA. Therefore we can say that the AMD Athlon and Core 2 Duo processors are based on the same ISA but have different microarchitectures with different performance and efficiencies.

## Slide 46
Multiprocessors
A shared-memory multiprocessor (or just multiprocessor henceforth) is a computer system in which two or more CPUs share full access to a common RAM.
A program running on any of the CPUs sees a normal (usually paged) virtual address space.

## Slide 47
The only unusual property this system has is that the CPU can write some value into a memory word and then read the word back and get a different value (because another CPU has changed it).

## Slide 48
Multiprocessor architectures
Two or more CPUs and one or more memory modules all use the same bus for communication. When a CPU wants to read a memory word, it first checks to see if the bus is busy. If the bus is idle, the CPU puts the address of the word it wants on the bus, asserts a few control signals, and waits until the memory puts the desired word on the bus.

## Slide 49
ProbIem to previous approach, If the bus is busy when a CPU wants to read or write memory, the CPU just waits until the bus becomes idle.
The cache can be inside the CPU chip, next to the CPU chip, on the processor board, or some combination of all three.
Since many reads can now be satisfied out of the local cache, there will be much less bus traffic, and the system can support more CPUs.
(c) in this each CPU has not only a cache, but also a local, private memory which it accesses over a dedicated (private) bus.
To use this configuration optimally, the compiler should place all the program text, strings, constants and other read-only data, stacks, and local variables in the private memories.
The shared memory is then only used for writable shared variables.

## Slide 50
Types of Multiprocessors
There are mainly two types of multiprocessors i.e. symmetric and asymmetric
multiprocessors. Details about them are as follows:
• Symmetric Multiprocessors
ln these types of systems, each processor contains a similar copy of the operating system and they all communicate with each other. All the processors are in a peer to peer relationship i.e. no master - slave relationship exists between them.
An example of the symmetric multiprocessing system is the Encore version of Unix for the Multimax Computer.

## Slide 51
Types of Multiprocessors
• Asymmetric Multiprocessors
ln asymmetric systems, each processor is given a predefined task. There is a master processor that gives instruction to all the other processors. Asymmetric multiprocessor system contains a master slave relationship.
Asymmetric multiprocessor was the only type of multiprocessor available before symmetric multiprocessors were created. Now also, this is the cheaper option.

## Slide 52
Advantages of Multiprocessor Systems
There are multiple advantages to multiprocessor systems. Some of these are:
More reliable Systems In a multiprocessor system, even if one processor fails, the system will not halt. For example: If there are 5 processors in a multiprocessor system and one of them fails, then also 4 processors are still working. So the system only becomes slower and does not ground to a halt.
Enhanced Throughput If multiple processors are wDrking in tandem, then the throughput of the system increases i.e. number of processes getting executed per unit of time increase. If there are N processors then the throughput increases by an amount just under N.
More Economic Systems Multiprocessor systems are cheaper than single processor systems in the long run because they share the data storage, peripheral devices, power supplies etc. If there are multiple processes that share data, it is better to schedule them on multiprocessor systems with shared data than have different computer systems with muItipIe copies of the data.

## Slide 53
Disadvantages of Multiprocessor Systems
There are some disadvantages as well to multiprocessor systems. Some of
these are:
lncreased Expense Even though multiprocessor systems are cheaper in the long run than using multiple computer systems, still they are quite expensive. It is much cheaper to buy a simple single processor system than a multiprocessor system.
Complicated Operating System Required There are multiple processors in a multiprocessor system that share peripherals, memory etc. So, it is much more complicated to schedule processes and impart resources to processes, than in single processor systems. Hence, a more complex and complicated operating system is required in multiprocessor systems.
Large Main Memory Required All the processors in the multiprocessor system share the memory. So a much larger pool of memory is required as compared to single processor systems.

## Slide 54
Coupling of Processors
Tightly Coupled System
Tasks and/or processors communicate in a highly synchronized fashion
Communicates through a common shared memory
Shared memory system
Loosely Coupled System
Tasks cir processors do not communicate in a synchronized fashion
Communicates by message passing packets
Overhead for data exchange is high
Distributed memory system

## Slide 55
Interconnection Structure
The components that form a multiprocessor system are CPUs, IOPs connected to input-output devices, and a memory unit.
The interconnection between the components can have different physical configurations, depending on the number of transfer paths that are available.
Between the processors and memory in a shared memory system
Among the processing elements in a loosely coupled system
There are several physical forms available for establishing an interconnection network.
1. Time-shared common bus
2. Multiport memory
3. Crossbar switch

## Slide 56
Time Shared Common Bus
A common-bus multiprocessor system consists of a number of processors
connected through a common path to a memory unit.
Only one processor can communicate with the memory or another processor at any given time.
As a consequence, the total overall transfer rate within the system is limited by the speed of the single path.
A more economical implementation of a dual bus structure is depicted in Fig. below.
Part of the local memory may be designed as a cache memory attached to the CPU.

## Slide 57
MuItiport Memory
A multiport memory system employs separate buses between each memory module
and each CPU.
The module must have internal control logic to determine which port will have access to memory at any given time, Memory access conflicts are resolved by assigning fixed priorities to each memory port.
Adv..
The high transfer rate can be achieved because of the multiple paths.
Disadv.:
It requires expensive memory control logic and a large number of cables and
connections

## Slide 58
Cross Bar Switch
Consists of a number of crosspoints that ore placed ot intersections between processor buses and memory module paths.
The small square in each crosspoint is a switch thot determines the path /rom a processor to o memory module.
Adv.:
Supports simultaneous transfers from all memory modules
Disadv.:
The hardware required to implement the switch can become quite large and complex.
fig. shows the functional design of a crossbar switch connected to one memory module.