## Slide 1: Example
Major Components of CPU

## Slide 2
Central Processing Unit 2 Lecture 22
CSE 211, Computer Organization and Architecture
Overview
  Introduction
  General Register Organization
  Stack Organization
  Instruction Formats
  Addressing Modes
  Data Transfer and Manipulation
  Program Control and Program Interrupt
  Reduced Instruction Set Computer

## Slide 3
Central Processing Unit 3 Lecture 22
CSE 211, Computer Organization and Architecture
Major Components of CPU
Storage Components
Registers
Flags
Execution (Processing) Components
Arithmetic Logic Unit(ALU)
Arithmetic calculations, Logical computations, Shifts/Rotates
Transfer Components
Bus
Control Components
Control Unit

## Slide 4
Central Processing Unit 4 Lecture 22
CSE 211, Computer Organization and Architecture
Register
In Basic Computer, there is only one general purpose register, the Accumulator (AC)
In modern CPUs, there are many general purpose registers
It is advantageous to have many registers
  Transfer between registers within the processor are relatively fast
  Going “off the processor” to access memory is much slower
  Important:
How many registers will be the best ?

## Slide 6
Central Processing Unit 6 Lecture 22
CSE 211, Computer Organization and Architecture
General Register Organization
MUX
SELA
{
MUX
}
SELB
ALU
OPR
R1
R2
R3
R4
R5
R6
R7
Input
3 x 8
decoder
SELD
Load
(7 lines)
Output
A bus
B bus
Clock

## Slide 8
Central Processing Unit 8 Lecture 22
CSE 211, Computer Organization and Architecture
Operation of ControlUnit
The control unit
Directs the information flow through ALU by
- Selecting various Components in the system
- Selecting the Function of ALU
Example: R1  R2 + R3
[1] MUX A selector (SELA): BUS A  R2
[2] MUX B selector (SELB): BUS B  R3
[3] ALU operation selector (OPR): ALU to ADD
[4] Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
SELA
SELB
SELD
OPR
3
3
3
5
  Binary
  Code SELA SELB SELD
  000 Input Input None
  001 R1 R1 R1
  010 R2 R2 R2
  011 R3 R3 R3
  100 R4 R4 R4
  101 R5 R5 R5
  110 R6 R6 R6
  111 R7 R7 R7

## Slide 9
Central Processing Unit 9 Lecture 22
CSE 211, Computer Organization and Architecture
ALU Control
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
  R1  R2  R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100

## Slide 10
Central Processing Unit 10 Lecture 23
CSE 211, Computer Organization and Architecture
Stack Organization
Stack
Very useful feature for nested subroutines, nested interrupt services
Also efficient for arithmetic expression evaluation
Storage which can be accessed in LIFO
Pointer: SP
Only PUSH and POP operations are applicable
Stack Organization
  Register Stack Organization
  Memory Stack Organization

## Slide 11
Central Processing Unit 11 Lecture 23
CSE 211, Computer Organization and Architecture
Register Stack Organization
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
A
B
C
0
1
2
3
4
63
FULL
EMPTY
SP
DR
Flags
Stack pointer
6 bits
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP  1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0

## Slide 12
Central Processing Unit 12 Lecture 23
CSE 211, Computer Organization and Architecture
Memory Stack Organization
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
Memory with Program, Data,
and Stack Segments
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack
- Most computers do not provide hardware to check stack overflow (full
stack) or underflow (empty stack)  must be done in software

## Slide 13
Central Processing Unit 13 Lecture 23
CSE 211, Computer Organization and Architecture
Reverse Polish Notation
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 14
Central Processing Unit 14 Lecture 23
CSE 211, Computer Organization and Architecture
Processor Organization
In general, most processors are organized in one of 3 ways
  Single register (Accumulator) organization
    Basic Computer is a good example
    Accumulator is the only general purpose register
  General register organization
    Used by most modern computer processors
    Any of the registers can be used as the source or destination for computer operations
  Stack organization
    All operations are done using the hardware stack

## Slide 15
Central Processing Unit 15 Lecture 24
CSE 211, Computer Organization and Architecture
Instruction Format
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - determines how the address field is to be interpreted (to
get effective address or the operand)
The number of address fields in the instruction format depends on the internal organization of CPU
Instruction Fields

## Slide 16
Central Processing Unit 16 Lecture 24
CSE 211, Computer Organization and Architecture
Instruction Format
The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD

## Slide 17
Central Processing Unit 17 Lecture 24
CSE 211, Computer Organization and Architecture
Three & Two Address Instruction
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[B] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 18
Central Processing Unit 18 Lecture 24
CSE 211, Computer Organization and Architecture
One Address Instruction
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */

## Slide 19
Central Processing Unit 19 Lecture 24
CSE 211, Computer Organization and Architecture
Zero Address Instruction
Zero-Address Instructions
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 20
Addressing Modes

## Slide 21
Central Processing Unit 21 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
Addressing Modes
- Specifies a rule for interpreting or modifying the address field of the instruction (before the operand is actually referenced)
- Variety of addressing modes
- to give programming flexibility to the user
- to use the bits in the address field of the instruction efficiently

## Slide 22
Central Processing Unit 22 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
1. Implied Mode
- Address of the operands are specified implicitly in the definition of the instruction
- No need to specify address in the instruction
- EA = AC, or EA = Stack[SP]
- Examples from Basic Computer - CLA, CME, INP
2. Immediate Mode
- Instead of specifying the address of the operand, operand itself is specified
- No need to specify address in the instruction
- However, operand itself needs to be specified
- Sometimes, require more bits than the address
- Fast to acquire an operand

## Slide 23
Central Processing Unit 23 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
3. Register Mode
- Address specified in the instruction is the register address
- Designated operand need to be in a register
- Shorter address than the memory address
- Saving address field in the instruction
- Faster to acquire an operand than the memory addressing
- EA = IR(R) (IR(R): Register field of IR)

## Slide 24
Central Processing Unit 24 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
4. Register Indirect Mode
- Instruction specifies a register which contains the memory address of the operand
- Saving instruction bits since register address is shorter than the memory address
- Slower to acquire an operand than both the register addressing or memory addressing
- EA = [IR(R)] ([x]: Content of x)
5. Autoincrement or Autodecrement Mode
- When the address in the register is used to access memory, the value in the register is incremented or decremented by 1 automatically

## Slide 25
Central Processing Unit 25 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
6. Direct Address Mode
- Instruction specifies the memory address which can be used directly to access the memory
- Faster than the other memory addressing modes
- Too many bits are needed to specify the address for a large physical memory space
- EA = IR(addr) (IR(addr): address field of IR)

## Slide 26
Central Processing Unit 26 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
7. Indirect Addressing Mode
- The address field of an instruction specifies the address of a memory location that contains the address of the operand
- When the abbreviated address is used large physical memory can be addressed with a relatively small number of bits
- Slow to acquire an operand because of an additional memory access
- EA = M[IR(address)]

## Slide 27
Central Processing Unit 27 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
8. Relative Addressing Modes
- The Address fields of an instruction specifies the part of the address (abbreviated address) which can be used along with a designated register to calculate the address of the operand
- Address field of the instruction is short
- Large physical memory can be accessed with a small number of address bits
- EA = f(IR(address), R), R is sometimes implied

## Slide 28
Central Processing Unit 28 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode
3 different Relative Addressing Modes depending on R;
PC Relative Addressing Mode (R = PC)
- EA = PC + IR(address)
Indexed Addressing Mode (R = IX, where IX: Index Register)
- EA = IX + IR(address)
Base Register Addressing Mode
(R = BAR, where BAR: Base Address Register)
- EA = BAR + IR(address)

## Slide 29
Central Processing Unit 29 Lecture 25
CSE 211, Computer Organization and Architecture
Addressing Mode - Example
Addressing
Mode
Effective
Address
Content
of AC
  Direct address 500 /* AC  (500) */ 800
  Immediate operand - /* AC  500 */ 500
  Indirect address 800 /* AC  ((500)) */ 300
  Relative address 702 /* AC  (PC+500) */ 325
  Indexed address 600 /* AC  (RX+500) */ 900
  Register - /* AC  R1 */ 400
  Register indirect 400 /* AC  (R1) */ 700
  Autoincrement 400 /* AC  (R1)+ */ 700
  Autodecrement 399 /* AC  -(R) */ 450
Load to AC Mode
Address = 500
Next instruction
200
201
202
399
400
450
700
500
800
600
900
702
325
800
300
Memory
Address
PC = 200
R1 = 400
XR = 100
AC

## Slide 30
Central Processing Unit 30 Lecture 26
CSE 211, Computer Organization and Architecture
Data Transfer Instructions
Load LD
Store ST
Move MOV
Exchange XCH
Input IN
Output OUT
Push PUSH
Pop POP
Name Mnemonic
Typical Data Transfer Instructions

## Slide 31
Central Processing Unit 31 Lecture 26
CSE 211, Computer Organization and Architecture
Data Transfer Instructions
Direct address LD ADR AC M[ADR]
Indirect address LD @ADR AC  M[M[ADR]]
Relative address LD $ADR AC  M[PC + ADR]
Immediate operand LD #NBR AC  NBR
Index addressing LD ADR(X) AC  M[ADR + XR]
Register LD R1 AC  R1
Register indirect LD (R1) AC  M[R1]
Autoincrement LD (R1)+ AC  M[R1], R1  R1 + 1
Autodecrement LD -(R1) R1  R1 - 1, AC  M[R1]
Mode
Assembly
Convention
Register Transfer
Data Transfer Instructions with Different Addressing Modes

## Slide 32
Central Processing Unit 32 Lecture 26
CSE 211, Computer Organization and Architecture
Data Maniplulation Instructions
Three Basic Types:
Arithmetic instructions
Logical and bit manipulation instructions
Shift instructions

## Slide 33
Central Processing Unit 33 Lecture 26
CSE 211, Computer Organization and Architecture
Data Manipulation Instructions
Arithmetic Instructions
Name Mnemonic
Increment INC
Decrement DEC
Add ADD
Subtract SUB
Multiply MUL
Divide DIV
Add with Carry ADDC
Subtract with Borrow SUBB
Negate(2’s Complement) NEG

## Slide 34
Central Processing Unit 34 Lecture 26
CSE 211, Computer Organization and Architecture
Data Manipulation Instructions
Clear CLR
Complement COM
AND AND
OR OR
Exclusive-OR XOR
Clear carry CLRC
Set carry SETC
Complement carry COMC
Enable interrupt EI
Disable interrupt DI
Name Mnemonic
Logical and Bit Manipulation Instructions

## Slide 35
Central Processing Unit 35 Lecture 26
CSE 211, Computer Organization and Architecture
Data Manipulation Instructions
Logical shift right SHR
Logical shift left SHL
Arithmetic shift right SHRA
Arithmetic shift left SHLA
Rotate right ROR
Rotate left ROL
Rotate right thru carry RORC
Rotate left thru carry ROLC
Name Mnemonic
Shift Instructions

## Slide 36
Central Processing Unit 36 Lecture 27
CSE 211, Computer Organization and Architecture
Program Control Instruction
PC
+1
In-Line Sequencing (Next instruction is fetched from the next adjacent location in the memory)
Address from other source; Current Instruction, Stack, etc; Branch, Conditional Branch, Subroutine, etc
Program Control Instructions
Name Mnemonic
Branch BR
Jump JMP
Skip SKP
Call CALL
Return RTN
Compare(by  ) CMP
Test(by AND) TST
* CMP and TST instructions do not retain their
results of operations (  and AND, resp.).
They only set or clear certain Flags.

## Slide 37
Central Processing Unit 37 Lecture 27
CSE 211, Computer Organization and Architecture
Conditional Branch Instruction
BZ Branch if zero Z = 1
BNZ Branch if not zero Z = 0
BC Branch if carry C = 1
BNC Branch if no carry C = 0
BP Branch if plus S = 0
BM Branch if minus S = 1
BV Branch if overflow V = 1
BNV Branch if no overflow V = 0
BHI Branch if higher A > B
BHE Branch if higher or equal A  B
BLO Branch if lower A < B
BLOE Branch if lower or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
BGT Branch if greater than A > B
BGE Branch if greater or equal A  B
BLT Branch if less than A < B
BLE Branch if less or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
Unsigned compare conditions (A - B)
Signed compare conditions (A - B)
Mnemonic Branch condition Tested condition

## Slide 38
Central Processing Unit 38 Lecture 27
CSE 211, Computer Organization and Architecture
Subroutine Call and Return
Call subroutine
Jump to subroutine
Branch to subroutine
Branch and save return address
Fixed Location in the subroutine (Memory)
Fixed Location in memory
In a processor Register
In memory stack
- most efficient way
Subroutine Call
Two Most Important Operations are Implied;
* Branch to the beginning of the Subroutine
- Same as the Branch or Conditional Branch
* Save the Return Address to get the address of the location in the Calling Program upon
exit from the Subroutine
Locations for storing Return Address
CALL
SP  SP - 1
M[SP]  PC
PC  EA
RTN
PC  M[SP]
SP  SP + 1

## Slide 39
Central Processing Unit 39 Lecture 27
CSE 211, Computer Organization and Architecture
Flag, Processor Status Word
In Basic Computer, the processor had several (status) flags –
  1 bit value that indicated various information about the processor’s state – E, FGI, FGO, I, IEN, R
In some processors, flags like these are often combined into a register
  – the processor status register (PSR); sometimes called a processor status word (PSW)
Status Flag Circuit
c7
c8
A B
8 8
8-bit ALU
V Z S C
F7
F7 - F0
8
F
Check for
zero output

## Slide 40
Central Processing Unit 40 Lecture 27
CSE 211, Computer Organization and Architecture
Flag, Processor Status Word
Common flags in PSW are
  C (Carry): Set to 1 if the carry out of the ALU is 1
  S (Sign): The MSB bit of the ALU’s output
  Z (Zero): Set to 1 if the ALU’s output is all 0’s
  V (Overflow): Set to 1 if there is an overflow
Status Flag Circuit
c7
c8
A B
8 8
8-bit ALU
V Z S C
F7
F7 - F0
8
F
Check for
zero output

## Slide 41
Central Processing Unit 41 Lecture 27
CSE 211, Computer Organization and Architecture
Program Interrupt
Types of Interrupts
External interrupts
External Interrupts initiated from the outside of CPU and Memory
- I/O Device → Data transfer request or Data transfer complete
- Timing Device → Timeout
- Power Failure
- Operator
Internal interrupts (traps)
Internal Interrupts are caused by the currently running program
- Register, Stack Overflow
- Divide by zero
- OP-code Violation
- Protection Violation

## Slide 42
Central Processing Unit 42 Lecture 27
CSE 211, Computer Organization and Architecture
Program Interrupt
Types of Interrupts
Software Interrupts
Both External and Internal Interrupts are initiated by the computer HW.
Software Interrupts are initiated by the executing an instruction.
- Supervisor Call 1. Switching from a user mode to the supervisor mode
2. Allows to execute a certain class of operations
which are not allowed in the user mode

## Slide 43
Central Processing Unit 43 Lecture 27
CSE 211, Computer Organization and Architecture
Interrupt Procedure
  - The interrupt is usually initiated by an internal or an external signal rather than from the execution of an instruction (except for the software interrupt)
  - The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction
  - An interrupt procedure usually stores all the information necessary to define the state of CPU rather than storing only the PC.
Interrupt Procedure and Subroutine Call

## Slide 44
Central Processing Unit 44 Lecture 27
CSE 211, Computer Organization and Architecture
Interrupt Procedure
  The state of the CPU is determined from:
      Content of the PC
      Content of all processor registers
      Content of status bits
      Many ways of saving the CPU state
      Depending on the CPU architectures
Interrupt Procedure and Subroutine Call

## Slide 46
Central Processing Unit 46 Lecture 28
CSE 211, Computer Organization and Architecture
IBM System/360, 1964
The real beginning of modern computer architecture
Distinction between Architecture and Implementation
Architecture: The abstract structure of a computer seen by an assembly-language programmer
Continuing growth in semiconductor memory and microprogramming
 A much richer and complicated instruction sets
 CISC(Complex Instruction Set Computer)
High-Level
Language
Instruction
Set
Hardware
Compiler
-program
Architecture
Implementation
Hardware
Hardware
RISC- Historical BackGround

## Slide 47
Central Processing Unit 47 Lecture 28
CSE 211, Computer Organization and Architecture
Arguments Advanced at that time
  Richer instruction sets would simplify compilers
  Richer instruction sets would alleviate the software crisis
    move as much functions to the hardware as possible
  Richer instruction sets would improve architecture quality
These computers with many instructions and addressing modes came to be known as Complex Instruction Set Computers (CISC)
One goal for CISC machines was to have a machine language instruction to match each high-level language statement type
CISC
CISC

## Slide 48
Central Processing Unit 48 Lecture 28
CSE 211, Computer Organization and Architecture
Complex Instruction Set Computers
Another characteristic of CISC computers is that they have instructions that act directly on memory addresses
  For example, ADD L1, L2, L3 that takes the contents of M[L1] adds it to the contents of M[L2] and stores the result in location M[L3]
An instruction like this takes three memory access cycles to execute
That makes for a potentially very long instruction execution cycle

## Slide 49
Central Processing Unit 49 Lecture 28
CSE 211, Computer Organization and Architecture
Complex Instruction Set Computers
The problems with CISC computers are
  The complexity of the design may slow down the processor,
  The complexity of the design may result in costly errors in the processor design and implementation,
  Many of the instructions and addressing modes are used rarely, if ever

## Slide 50
Central Processing Unit 50 Lecture 28
CSE 211, Computer Organization and Architecture
Summary : Criticism On CISC
High Performance General Purpose Instructions
1. Complex Instruction
→ Format, Length, Addressing Modes
→ Complicated instruction cycle control due to the complex decoding HW and decoding process
2. Multiple memory cycle instructions
→ Operations on memory data
→ Multiple memory accesses/instruction

## Slide 51
Central Processing Unit 51 Lecture 28
CSE 211, Computer Organization and Architecture
Summary : Criticism On CISC
High Performance General Purpose Instructions
3. Microprogrammed control is necessity
→ Microprogram control storage takes substantial portion of CPU chip area
→ Semantic Gap is large between machine instruction and microinstruction
4. General purpose instruction set includes all the features required by individually different applications
→ When any one application is running, all the features required by the other applications are extra burden to the application

## Slide 52
Central Processing Unit 52 Lecture 28
CSE 211, Computer Organization and Architecture
RISC – Reduced Instruction Set Computers
In the late ‘70s and early ‘80s there was a reaction to the shortcomings of the CISC style of processors
Reduced Instruction Set Computers (RISC) were proposed as an alternative
The underlying idea behind RISC processors is to simplify the instruction set and reduce instruction execution time

## Slide 53
Central Processing Unit 53 Lecture 28
CSE 211, Computer Organization and Architecture
RISC – Reduced Instruction Set Computers
RISC processors often feature:
  Few instructions
  Few addressing modes
  Only load and store instructions access memory
  All other operations are done using on-processor registers
  Fixed length instructions
  Single cycle execution of instructions
  The control unit is hardwired, not microprogrammed

## Slide 54
Central Processing Unit 54 Lecture 28
CSE 211, Computer Organization and Architecture
RISC – Reduced Instruction Set Computers
Since all but the load and store instructions use only registers for operands, only a few addressing modes are needed
By having all instructions the same length, reading them in is easy and fast
The fetch and decode stages are simple
The instruction and address formats are designed to be easy to decode

## Slide 55
Central Processing Unit 55 Lecture 28
CSE 211, Computer Organization and Architecture
RISC – Reduced Instruction Set Computers
Unlike the variable length CISC instructions, the opcode and register fields of RISC instructions can be decoded simultaneously
The control logic of a RISC processor is designed to be simple and fast
The control logic is simple because of the small number of instructions and the simple addressing modes
The control logic is hardwired, rather than microprogrammed, because hardwired control is faster